## Slide 1
DREAM EndCap detector, engineering specifications
Irina Stefanescu
ESS DG

## Slide 2
beam
sample
Backward detector, “EndCap”
Mantle detector
Forward detector (identical with the Backward detector)
The DREAM detector system
SANS tank +
Detector (TBD)
HR detector (TBD)
Background information

## Slide 3
The DREAM backward (EndCap) & forward detectors
It is an assembly of 12°-sectors, each sector consisting of 4 detector modules (SUMOs)
SUMO = SUper MOdule
2θ
𝞅
beam
12°-sector

## Slide 4
4 SUMO modules mounted on the same backplate = mounting unit
SUMO3
SUMO6
Engineering design of the 12°- sector
The DREAM 12°- sector @V20
138°
166°
2Θ~7°
𝞅=12°
Neutron beam

## Slide 5
SUMO3
SUMO4
SUMO5
SUMO6
16 wires
16 equal strips
4 segments x 2
6 segments x 2
8 segments x 2
10 segments x 2
segment

## Slide 6
SUMO3
SUMO4
SUMO5
SUMO6
Segmentation must ensure that all voxels deliver the same angular resolution Δθ=0.36°
16*16*8 voxels
16 wires
16 equal strips
16*16*10 voxels
16*16*12 voxels
16*16*20 voxels

## Slide 7
Height front (Gy1)
Height back (Gy2)
Sensitive depth (Gz)
Width front bottom (Gx1)
Width front top (Gx3)
Width back top (Gx4)
Width back bottom (Gx2)
Main design (engineering) parameters for the SUMOs
 | SUMO3 | SUMO4 | SUMO5 | SUMO6
No of cassettes/module | 4 | 6 | 8 | 10
No of counters per module (no of cassettes x 2) | 4x2 | 6x2 | 8x2 | 10x2
No of strips/counter | 16 | 16 | 16 | 16
No of wires/counter | 16 | 16 | 16 | 16
No of (non-identical) voxels/counter | 16x16 | 16x16 | 16x16 | 16x16
No of voxels/SUMO | 4x2x16x16 | 6x2x16x16 | 8x2x16x16 | 10x2x16x16
Engineering specifications, see photos/cartoons for definitions |  |  |  | 
2θ-scattering angle of the module [deg] | 7.6 | 7.1 | 6.7 | 6.4
2θ-scattering angle covered by the module [deg] | 139-146.6 | 145-152 | 151-158 | 158-165
Radial distance of the sensitive volume from the scattering center [mm] | 1176 | 1249 | 1341 | 1460
Module sensitive depth (Gz) [mm] | 290 | 310 | 324 | 345
Width strip [mm] | =290/16 | =310/16 | =324/16 | =345/16
Thickness cathode strips [um] | 300 | 300 | 300 | 300
Thickness detector housing [um] | 300 | 300 | 300 | 300
Module height front (Gy1) [mm] | 159 | 157 | 160 | 165
Module height back (Gy2) [mm] | 184 | 199 | 201 | 214
Module width top front (Gx3) [mm] | 90 | 124 | 161 | 201
Module width top back (Gx4) [mm] | 103 | 147 | 195 | 243
Module width bottom front (Gx1) [mm] | 57.5 | 93 | 130 | 171
Module width bottom back (Gx2) [mm] | 65.4 | 107 | 145 | 204
Tilt angle module around Y-axis [deg] | 10 | 10 | 10 | 10
Tilt angle module around X-axis [deg] | 10 | 16 | 23 | 30
In the GEANT4 simulations the widths and heights of the individual cassettes of a specific SUMOs were calculated as the ratio
width (heights) module/no of cassettes in SUMO